## Slide 1: MONIMAN An overview of the current development BST/GBT/BK

## Slide 2: MONIMAN
Modern Development Technologies
State-Of-The-Art Scientific Domain Knowledge
Geotechnical Best-practices
PLAXIS Python scripting API
Qt Designer & PyQt5 GUI
Modularized object-oriented Python programming
Librabry based properties and features for soils, anchors, struts, etc.
Process automation for creating calculation steps
Monitoring data incorporation
Geotechnical sensitivity analysis and back-analysis
Cost-driven design optimization
Metamodeling and machine learning approaches

## Slide 3: MONIMAN
MONIMAN
Monitoring
data
Model creation
Model sensitivity analysis
Model updating
Cost-driven design optimization
Prognosis
Site
Digital twin (FEM calculation model)

## Slide 4: MONIMAN
Plaxman
Sensiman
Backman
Optiman
Automate PLAXIS input and customize PLAXIS output
Back-calculate soil parameters by fitting modeled outputs to measurements
Perform sensitivity analysis of soil/structure parameters to the system
Optimize costs and system performance
GUI & Utilities
User interface/ Communications/ File utilities/ Visualization utilities/ Saving and loading

## Slide 5: MONIMAN – Plaxman
DESIGN PRINCIPLES:
Use PLAXIS scripting interface to interact with PLAXIS kernel more intensively
Use modern Python modules to manage a user-friendly GUI windows
Create material and structrue libraries based on literature and our engineering best practices
Try to balance: Complexity – Purpose – Ease-of-use
EXPECTATIONS:
Fully functional PLAXIS2D model (for retaining wall systems)
Model creation time is reduced to minutes
A Python script of the model for further use in Sensitivity- and Backanalysis, and Optimization

## Slide 6: MONIMAN – Sensiman
How much is the influence of each model parameter to wall deflection?
Soil 1:
Soil 2:
Soil 3:
Sensitivity score w.r.t. parameter
for 1 measured point:
Total sensitivity score w.r.t.
parameter for all measured points:
Choose the most sensitive parameters for performing back-analysis.

## Slide 7: MONIMAN – Sensiman
Soil 1:
Soil 2:
Soil 3:
Field measurement
How to best visualize results?
This is a kind of back-analysis by brute-force search and visual inspection.

## Slide 8: MONIMAN – Backman
Soil 1:
Soil 2:
Soil 3:
Inclinometer:
PLAXIS:
Back-analysis is to fit to by repeatedly changing soil/ structure parameters by an optimization algorithm.
Back-analysis is a challenging ill-posed inverse problem:
Measurement noise
Soil variabilities (inhomogeinity) and mechanical behaviors that are not captured by soil models (anisotropy)
Other modeling uncertainties (soil-struction interactions, no real loads)
Many optimization strategies: Kalman filters (KF), Particle swarm optimization (PSO), etc.
Metamodeling and machine learning approach to build a surrogate model that is faster than the FEM model.
Intelligent algorithms and automated process themselves help to back-calculate soil/ structure parameters in such a short time as possible.

## Slide 9: MONIMAN – Optiman
Automated design optimization process taking into account material and execution costs.
How far can we go to reach most economic design?

## Slide 10: MONIMAN
Plaxman
Sensiman
Backman
Optiman
Automate PLAXIS input and customize PLAXIS output
Back-calculate soil parameters by fitting modeled outputs to measurements
Perform sensitivity analysis of soil/structure parameters to the system
Optimize costs and system performance
GUI & Utilities
User interface/ Communications/ File utilities/ Visualization utilities/ Saving and loading
5 months
~20 000 lines of code

## Slide 11: MONIMAN
Development Technologies
Scientific Domain Knowledge
Geotechnical Best-practices
MONIMAN
Monitoring
data
Model creation
Model sensitivity analysis
Model updating
Cost-driven design optimization
Prognosis
Site
Digital twin (FEM calculation model)
MONIMAN: Optimization-based tool to turn monitoring data into valuable design parameters that can help minimize the cost while securing the safe design.