## Slide 1: MONIMAN An overview of the current development BST/GBT/BK 03.2019

## Slide 2: MONIMAN
Modern Development Tools
State-Of-The-Art Scientific Domain Knowledge
Geotechnical Best-practices
PLAXIS Python scripting API
Qt Designer & PyQt5 GUI
Modularized object-oriented Python programming
Librabry based properties and features for soils, anchors, struts, etc.
Process automation for creating calculation steps
Monitoring data incorporation
Geotechnical sensitivity analysis and back-analysis
Cost-driven design optimization
Metamodeling and machine learning approaches

## Slide 3: MONIMAN
MONIMAN
Monitoring
data
Model creation
Model sensitivity analysis
Model updating (back-analysis)
Cost-driven design optimization
Prognosis
Site
Digital twin (FEM calculation model)

## Slide 4: MONIMAN
Plaxman
Sensiman
Backman
Optiman
Automate PLAXIS Input & Output
Back-calculate soil parameters by fitting modeled outputs to site measurements
Perform sensitivity analysis of soil/structure parameters to the system
Optimize costs and system performance
GUI & Utilities
User interface/ Communications/ File utilities/ Visualization utilities/ Saving and loading

## Slide 5: MONIMAN – Plaxman
Predefined soils/ structures to load
Model creation time is reduced to minutes
Fully functional: Soils>Structures>Phases>Outputs
A Python script of the model for further use in
Sensitivity analylsis,
Backanalysis, and
Design optimization
Plaxis Remote Scripting with Python
Reference project in Beirut

## Slide 6: MONIMAN – Plaxman
Predefined soils/ structures to load
Model creation time is reduced to minutes
Fully functional: Soils>Structures>Phases>Outputs
Requested graphical and numerical outputs for dimensioning
Repeated model evalutions with updated model parameters for sensitivity analysis, back-analysis, and design optimizatoin.
Plaxis Remote Scripting with Python
Reference project in Beirut

## Slide 7: MONIMAN – Sensiman
How much is the influence of each model parameter to wall deflection?
Soil 1:
Soil 2:
Soil 3:
Sensitivity score w.r.t. parameter
for 1 measured point:
Total sensitivity score w.r.t.
parameter for all measured points:
Choose the most sensitive parameters for performing back-analysis.
Sensitivity analysis of system parameters to certain system responses

## Slide 8: MONIMAN – Sensiman
Local sensitivity analyiss
Exc.

## Slide 9: MONIMAN – Sensiman
Local sensitivity analyiss
Exc.

## Slide 10: MONIMAN – Sensiman
Metamodel instead of FE model
Gaussian process (GP)
(Rasmussen and Williams, 2006)
Proper orthogonal decomposition (POD) + radial basis function (RBF) (Khaledi and Schanz, 2014)
On-going Master‘s thesis work: Mohammad Sanayei
Notes: Williams, C.K. and Rasmussen, C.E., 2006. Gaussian processes for machine learning. Cambridge, MA: MIT Press.
Khaledi, K., Schanz, T. and Miro, S., 2014. Application of metamodelling techniques for mechanized tunnel simulation. Journal of Theoretical and Applied Mechanics, 44(1), pp.45-54.

## Slide 11: MONIMAN – Sensiman
Metamodel instead of FE model
Metamodeling by Gaussian Process using 250 training samples + 30 testing samples
Evaluation time:
FE model : ~4 min.
Metamodel: ~1 millisec.

## Slide 12: MONIMAN – Sensiman
Metamodel instead of FE model
FE Model (PLAXIS)
Random sets of model parameters
Observables (Target data)
Metamodel
(GP, POD)
Metamodel
(GP, POD)
Senstivity analysis
Back-analysis
Design/ cost optimization
X
Y
Model training
Sampling
Model validation
Model deployment
Why is metamodel beneficial?
Well-designed random sampling method (such as Latin Hypercube) helps reduce the sampling size yet cover the design (parameter) space
The result of one-time upfront efforts (FE simulations + training + validation) is used for demanding investigations that follow (sensitivity, back-analysis, design optimization)

## Slide 13: MONIMAN – Backman
Soil 1:
Soil 2:
Soil 3:
Inclinometer:
PLAXIS:
Back-analysis is to fit to by repeatedly changing soil/ structure parameters by an optimization algorithm.
Back-analysis is a challenging ill-posed inverse problem:
Measurement noise
Soil variabilities (inhomogeinity) and mechanical behaviors that are not captured by soil models (anisotropy)
Other modeling uncertainties (soil-structure interactions, no real loads)
Many numerical optimization algorithms: Kalman filters (KF), Particle swarm optimization (PSO), etc.
Numerical algorithms back-calculate soil/ structure parameters by fitting modeled outputs to measured site data using as few model evaluations as possible.
Geotechnical back-analysis

## Slide 14: MONIMAN – Backman
Kalman filter for geotechnical back-analysis
Nguyen, L.T., Nestorović, T., Hölter, R. and Schanz, T., Identifying the geological scenario ahead of the tunnel face: The use of elastoplastic and elastodynamic responses. Geotec Hanoi 2016.

## Slide 15: MONIMAN – Backman
Kalman filter for geotechnical back-analysis

## Slide 16: MONIMAN – Backman
Kalman filter for geotechnical back-analysis

## Slide 17: MONIMAN – Backman
Kalman filter for geotechnical back-analysis

## Slide 18: MONIMAN – Backman
Kalman filter for geotechnical back-analysis
Parameter | Initial | Back-calculated | True | Deviation (%)
Gref_2 [kN/m^2] | 71968,98 | 63751,30 | 57692,30 | 9,50
Phi_2 [deg.] | 27,05 | 21,64 | 22,00 | 1,66
Gref_3 [kN/m^2] | 12193,90 | 87626,38 | 88461,53 | 0,95
Cref_3 [kN/m^2] | 144,54 | 143,13 | 150,00 | 4,79
Phi_3 [deg.] | 36,58 | 26,81 | 27,50 | 2,57
4 iterations * (2*number_of_parameters + 1) = 44 PLAXIS2D runs
target
initial
back-calculated

## Slide 19: MONIMAN – Backman
https://cosmo-docs.phys.ethz.ch/cosmoHammer/user/pso.html
Particle swarm optimization (PSO) for geotechnical back-analysis
Typical back-analysis‘ multi-minima objective function
On-going Master‘s thesis work: Mohammad Sanayei

## Slide 20: MONIMAN – Optiman
Automated design optimization process taking into account material and execution costs.
How far can we go to reach most economic design while still satisfying system behavior?
Design/ cost optimization

## Slide 21: MONIMAN
Plaxman
Sensiman
Backman
Optiman
Model creation
Calculation and output
Kalman filter
Particle swarm opt.
Sensitivity analysis
Metamodeling
Design optimization
GUI & Utilities
User interface
File management Visualization and report
6 months
20420 code lines
Modern development framework and librabries (OOP Python, PyQt5, numpy, matplotlib, pickle, json, etc.) help shorten development time
Modularized structure helps in mantainaning and extending functionalities of MONIMAN
Careful use of results in scientific publications and public-domain resources can be beneficial
User experience and feedback are valuable
Numbers
Lessons learned

## Slide 22: MONIMAN
MONIMAN: Optimization-based tool to turn monitoring data into valuable design parameters that can help to minimize the cost while securing safe design.
MONIMAN
Monitoring
data
Model creation
Model sensitivity analysis
Model updating
Cost-driven design optimization
Prognosis
Site
Digital twin (FEM calculation model)

## Slide 23: Thanks to members of the BK Department for great support and input! Thank you for your listening! Your comments/ questions are welcome.